## Slide 1: UART Thou Mad?
Mickey and Toby

## Slide 2: Legal Notice Our opinion is our own. It DOES NOT IN ANY WAY represent the view of our employers.

## Slide 3
whoami - Mickey

## Slide 4
whoami - Toby

## Slide 5: Agenda
Intro
UART
  Background
  Finding it
Embedded systems overview
Tools overview
UART’s greatest hits
Look what we can do
Protecting your embedded device
Conclusion

## Slide 6: Intro
This talk is about sharing our experience
  WINs
  FAILs
Teach you a little bit more about how to use this feature to feed your curiosity

## Slide 7: UART Background
UART = Universal Asynchronous Receiver/Transmitter
  What is it? Who knows! We think it might be gnomes.
  Where did it come from?
    Heaven?
    Gordon Bell is referenced as designing UART interfaces for the PDP series.
  What matters is what goes through it.
    Data. Raw data.
      Between various components in a device
  And how embedded OSs treat it
    Frequently as a TTY or Console
Notes: Component examples – GPS to CPU,

## Slide 8: UART Background cont.
What is it for?
  Officially - translating data between parallel and serial formats.
  In practice
    Providing interconnect between components
    Providing a debug console interface for embedded devices
Why not just use JTAG?
  UART doesn’t play hard to get
    Less complex
    Doesn’t require a debugger
    No need to know assembly

## Slide 9: Finding UART
Look for four pins that look something like this:

## Slide 10: More Finding UART
Frequently the pins are tagged like this
That’s
  3.3v
  RX
  TX
  GND

## Slide 11: (slightly) Advanced Finding UART
Find “interesting” pins or pads in a row
  Almost always a group of four
Find ground (how? More about that later)
Warning! Make sure the voltage isn’t too high for your tools
Connect Ground to your tool (probably a BusPirate™)
Boot the device
While booting, touch the remaining pads/pins with your RX line one at a time
  Going to require multiple reboots
See something that isn’t garbage? Win!
Notes: Mickey will explain “interesting”

## Slide 12: Embedded Systems
Made out of flash, RAM and an SoC
    Samsung 512 Mb mobile DRAM
    Micron 2 Gb NAND flash memory
    Texas Instruments Sitara ARM Cortex A8 microprocessor

## Slide 13: Embedded Systems
Usual configuration on PCB's (test point grouped together the same way)
  (ab)Using the UART interface
OS will vary depending on vendor preference
  Linux
  RTOS of some flavor

## Slide 14: Embedded Systems
NOT JUST ROUTERS, there is a whole world of devices out there!
  Smart home power controllers
  WebCams
  HD TV streamers
  Set-top boxes
  Blueray players
  ….

## Slide 15: Tools Overview
FCC-ID database!
  It is your best friend in finding interesting devices
BusPirate
  Hardware hacker’s Swiss army knife

## Slide 16: Tools Overview
Multimeter
  This is how you find ground

## Slide 17: Tools Overview
USB-UART cable
  $8 on eBay
Soldering Iron
Magnifying Glass
Bright Light

## Slide 18: UART’s Greatest Hits
Oh look! Linux shell! Most devices simply boot to shell, no auth required.
  Some don't
Browsing the file system for interesting stuff (hidden_info.html)
Poking at it with an insider look - Seeing what happens on the inside, fuzzing devices and spotting the crash

## Slide 19: Look what we can do!
Oh, Look! We found a cert! - making firmware encryption benign. (Belkin WeMo hack)
Owning one device opened the door to others.
Fuzzing with UART monitoring for crashes

## Slide 20: Look what we can do!
Going to the dark side
Forensics? Changes via UART are volatile, reboot resets factory settings.
Using an Arduino with ethernet and UART to program the device in the field and leaving it there
  Demo

## Slide 21: Demo

## Slide 22: More Stuff to try
Writing scripts to make an embedded device evil…
  Throwable exploit platform
15$ Router on batteries acting as a pwn plug.

## Slide 23: Protecting your UART interface
Want to leave UART in?
  Boot to a login not a root shell
  Disable logging to system console
Remove UART interfaces all together
Belkin WeMo fix
  Upgraded firmware to require login to UART shell

## Slide 24: Conclusion
THIS IS SO MUCH FUN AND SIMPLE!
Why don't you have a go?